## Slide 1
Basic Electronics
Logic Gates

## Slide 2: Digital Electronics
Basic Digital circuits(AND, OR, NOT, NAND, NOR, EX-OR), Boolean Algebra, Examples of IC gates, Standard representation of IC gates
Half Adder, Full adder

## Slide 3: Logic Gates

## Slide 4: Universal Gates
The NAND and NOR gates are known as universal gates, because any logic function can be implemented using NAND or NOR gates

## Slide 5: Analyze Yourself
The logical inversion or complement is presented by the______ operator.
  NOT
  NAND
  NOR
  AND
The logical addition is presented by the _____ operator.
  AND
  OR
  NAND

## Slide 6: Analyze Yourself
3. The logical _____ is presented by the “AND” operator.
  Multiplication
  Addition
  Subtraction
4. The output of OR gate is zero when ________.
  Any one input is logic 1
  Two inputs are logic 1
  All inputs are logic 0

## Slide 7: Analyze Yourself
5. The 14-pin TTL integrated cuircuit with four, two inputs ______ gates inside, is IC 7432.
  OR
  AND
  NAND
6. The 14-pin TTL integrated circuit with four, two inputs ______ gates inside, is IC 7400.
  OR
  AND
NAND

## Slide 8: Analyze Yourself
7. The output of a ______ gate is 1 only when all of its inputs are 1.
  NOR
  EX-OR
  AND
  NOT
8. A NAND gate is equivalent to an AND gate plus a ____ gate put together.
  NOR
  NOT
  EX-OR

## Slide 9: Analyze Yourself
9. Logic states can be only be ______ or 0.
  3
  2
  1
  0
10. A 14 pin NOT gate IC has ______ NOT gates.
  8
  6
  5
  4

## Slide 10: DeMorgan’s Theorem
1. The Complement of a Product is equal to the Sum of the Complements.
2. The Complement of a Sum is equal to the Product of the Complements.

## Slide 11: Ex-OR can be used as Inverter
If we tie one input of an XOR Gate with Logic value ’1′ then XOR works as an Inverter
Here if we give input as
A=1 and B=X
Then Y=??????

## Slide 12: Implementation of logical expression
Implement following logical expression using NAND Gate
F = W.X.Y + X.Y.Z + Y.Z.W

## Slide 14: Analyze Yourself
11. ______ is the mathematical representation used to show the relation between the inputs and the outputs of a gate.
  Boolean expression
  Characteristic equation
  Both
12. The logic expression AB+ can be implemented by given inputs A and B to a two input _______.
  NOR
  Exclusive NOR gate
  Exclusive OR gate
  NAND gate

## Slide 15: Analyze Yourself
13. A∙(B+C)=AB+AC represents ________ law.
  Commutative
  Associative
  Distributive
14. (A∙B) ∙C= A∙(B∙C) represents ______ law.
  Commutative
  Associative
  Distributive

## Slide 16: Analyze Yourself
15. According to DeMorgan’s theorem : NOR = ______.
  Bubbled OR
  Bubbled NOR
  Bubbled AND
16. According to DeMorgan’s theorem : NAND = ______.
  Bubbled AND
  Bubbled NAND
  Bubbled OR

## Slide 17: Analyze Yourself
17. Standard two forms of Boolean expression are ____________.
  POS and POP
  POS and SOP
  SOP and SOS
18. Each individual term in standard SOP form is called ________.
  Literal
  Maxterm
  Minterm

## Slide 18: Half Adder
Input |  | Output | 
A | B | Carry | Sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Half adder equation needs two binary inputs and it produces two output sum and carry.
Half Adder
Carry = AB
Sum = A ex-or B
Output
B
A
Inputs
B

## Slide 19
Half Adder using Logic Gates

## Slide 20: Full Adder
Half Adder
Carry = AB+ A Cin +B Cin
Sum = A ex-or B ex-or Cin
Output
B
A
Inputs
Cin
Input |  |  | Output | 
A | B | Cin | Carry | Sum
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 21
Full Adder

## Slide 22
Full Adder using two Half Adder

## Slide 23: Analyze Yourself
19. The output of a ________ circuit at any instant of time is dependent only on the inputs present at that instant of time.
  Combinational
  Sequential
  Combinational and sequential
20. The output of a ________ circuit at any instant of time is dependent only on the present inputs as well as the past inputs/outputs.
  Combinational
  Sequential
  None of these

## Slide 24: Analyze Yourself
21. Sequential circuit contains ______.
  No memory element
  At least one memory element
  All inputs applied simultaneously
22. The _______ circuits do not contain any memory element.
  Combinational
  Sequential
  None of these

## Slide 25: Analyze Yourself
23. The result of binary addition 1+1 is _______.
  Carry 0, sum 0
  Carry 0, sum 1
  Carry 1, sum 0
  Carry 1, sum1
24. The result of binary addition 1+1+1 is ______.
  Carry 0, sum 0
  Carry 0, sum 1
  Carry 1, sum 0
  Carry 1, sum1